## Slide 1: Introduction to Manufacturing
Sagar Kamarthi
Associate Professor Dept. of Mechanical and Industrial Engineering
Northeastern University, Boston

## Slide 2: Topics
Product life cycle
Manufacturing
Building blocks of manufacturing

## Slide 3: Product Life Cycle
Concept
Design
Development
Production/ Manufacturing
Sale
Use
Reuse/Recycle
Distribution
Dispose
Product Life Cycle

## Slide 4: Product Life Cycle

## Slide 5: Design Part of Product Life Cycle

## Slide 6: Mfg Part of Life Cycle

## Slide 7: Topics
Product life cycle
Manufacturing
Building blocks of manufacturing

## Slide 8: Manufacturing
Manufacturing is the application of physical and chemical processes to alter the geometry, properties, and/or appearance of a given starting material
  To make parts or products, or
  To join multiple parts to make assembled products
Manufacturing adds value to the material
  When iron ore is converted to steel, value is added
  When sand is transformed into glass, value is added
  When crude oil is refined into petrol (gasoline), value is added

## Slide 9: Manufacturing Process

## Slide 10: Manufacturing Adds Value

## Slide 11: Building Blocks of Manufacturing
Materials
Manufacturing processes
Assembly operations
Manufacturing Automation

## Slide 12: Materials
Most engineering materials can be classified into one of four basic categories:
    Metals
    Ceramics
    Polymers
    Composites
Mechanical, physical and chemical properties these type of materials are different
These differences affect the manufacturing processes that can be used to produce products from them

## Slide 13: Metals
Metals are usually alloys, which are composed of two or more elements, at least one of which is metallic
Two basic groups of metals/alloys are:
  Ferrous metals are based on iron
    Comprises about 75% of metal tonnage in the world
    Steel = Fe‑C alloy (0.02 to 2.11% C)
    Cast iron = Fe-C alloy (2% to 4% C)
  Nonferrous metals are metallic elements and their alloys of aluminum, copper, magnesium, nickel, silver, tin, titanium, etc.

## Slide 14: Ceramics
Compounds containing metallic (or semi-metallic) and nonmetallic elements.
Typical nonmetallic elements are oxygen, nitrogen, and carbon
For processing, ceramics divide into:
  Crystalline ceramics
    Traditional ceramics, such as clay (hydrous aluminum silicates)
    Modern ceramics, such as alumina (Al2O3)
  Glasses
    Mostly based on silica (SiO2)

## Slide 15: Polymers
  Thermoplastic polymers
    They can be subjected to multiple heating and cooling cycles without altering their molecular structure
  Thermosetting polymers
    They cannot be reheated because molecules are chemically transformed (cured) into a rigid structure
  Elastomers
    They shows significant elastic behavior

## Slide 16: Composites
Nonhomogeneous mixtures of basic materials

## Slide 17: Manufacturing Processes
Material removal processes
  Starting material is a ductile or brittle solid
Solidification processes
  Starting material is a heated liquid or semi-fluid
Particulate processing
  Starting material consists of powders
Deformation processes
  Starting material is a ductile solid (commonly metal)

## Slide 18: Material Removal Processes
Excess material removed from the starting piece so what remains is the desired geometry
Examples: machining such as turning, drilling, and milling, grinding, laser cutting

## Slide 19: Material Removal Processes

## Slide 20
Metal chips fly in a high speed turning operation performed on a computer numerical control turning center (photo courtesy of Cincinnati Milacron).
©2007 John Wiley & Sons, Inc. M P Groover, Fundamentals of Modern Manufacturing 3/e

## Slide 21: Solidification Processes
Starting material is heated sufficiently to transform it into a liquid or highly plastic state
Examples: metal casting, injection molding

## Slide 22: Solidification Processes

## Slide 23: Solidification Processes

## Slide 24: A spectacular scene in steelmaking is charging of a basic oxygen furnace, in which molten pig iron produced in a blast furnace is poured into the BOF. Temperatures are around 1650°C (3000 ° F).

## Slide 25: Particulate Processing
Starting materials are powders of metals or ceramics
Usually involves pressing and sintering, in which powders are first compressed and then
Example: Kitchen tiles, ceramic plates

## Slide 26: Particulate Processing

## Slide 27: Deformation Processes
Starting workpart is shaped by application of forces that exceed the yield strength of the material
Examples: (a) forging, (b) extrusion

## Slide 28: Deformation Processes

## Slide 29: Deformation Processes
Sheet metal work is also a common deformation process

## Slide 30: Deformation Processes

## Slide 31: Assembly Operations
Two or more separate parts are assembled to form a product
Mechanical assembly fastens parts by mechanical methods
  Threaded fasteners (screws, bolts and nuts); press fitting, expansion fits

## Slide 32: Assembly Operations

## Slide 33
Assembly workers on an engine assembly line (photo courtesy of Ford Motor Company).
©2007 John Wiley & Sons, Inc. M P Groover, Fundamentals of Modern Manufacturing 3/e

## Slide 34
Assembly operations on the Boeing 777 (photo courtesy of Boeing Commercial Airplane Co.).
©2007 John Wiley & Sons, Inc. M P Groover, Fundamentals of Modern Manufacturing 3/e

## Slide 35: Automated Mfg Systems
Automated machine tools that process parts
Transfer lines that perform a series of machining operations
Automated assembly
Mfg Systems that use robots to perform processing and assembly operations
Automated material handling and storage systems
Automated inspection systems

## Slide 36: Advantages of Mfg Automation
Increase labor productivity
Reduce labor cost
Mitigate the effects of labor shortage
Reduce routine manual and clerical tasks
Improve worker safety
Improve product quality
Reduce manufacturing lead time
Improve manufacturing accuracy and tolerances
Enhance competitive edge

## Slide 37: Automation

## Slide 38: Automation Vs Production Volume